## Slide 1
E-PAGER
E-Pager: from monitoring alert to accountable incident response
A Spring Boot alerting and escalation backend that receives monitoring signals, validates trust, normalizes payloads, creates incidents, notifies the assigned user, and escalates if there is no acknowledgement.
Team-meet explanation deck: purpose, architecture, flows, security, testing, mobile readiness.
01
Vendor-independent alerts
Escalation matrix
Push notification tracking
Role security
Webhook HMAC

## Slide 2
PROBLEM FRAMING
Why E-Pager exists: monitoring tools alert, but humans need accountable escalation.
E-Pager technical deep dive | Source: project docs and implementation
02
Without E-Pager
- Grafana/Dynatrace produce tool-specific payloads
- Each integration would need custom logic
- Alert delivery and user acknowledgement are hard to prove
- Escalation is manual or tool-specific
- Security is scattered per source
With E-Pager
- One backend receives trusted alerts
- Source adapters normalize payloads
- Incident lifecycle becomes consistent
- Escalation matrix decides ownership
- Notification logs prove sent/received/seen
Core principle
Monitoring source can change, but incident, escalation, notification, and acknowledgement behavior should not change.
That is why raw Grafana/Dynatrace JSON is converted into UnifiedAlert before it touches core logic.

## Slide 3
SYSTEM MAP
Architecture keeps external alert formats outside the core incident workflow.
E-Pager technical deep dive | Source: project docs and implementation
03
Grafana
POST webhook
Raw JSON
Dynatrace
Custom problem
notification
Gateway
Validates bearer token
Signs E-Pager HMAC
Alert API
Validates source HMAC
Routes by source
Adapters
Grafana/Dynatrace -> UnifiedAlert
Incident
Create/update
TRIGGERED
Escalation
Assign level 1
schedule next
Notification
Create log
send push
track delivery
HMAC
token
signed
PostgreSQL persists users, policies, incidents, escalation events, devices, notification logs, delivery events, webhook audit, and refresh-token hashes.

## Slide 4
MODULE BOUNDARIES
Each package owns one responsibility and one failure boundary.
E-Pager technical deep dive | Source: project docs and implementation
04
Package
Positive path
Negative scenario handled
alert
Accept + normalize incoming alerts
Unknown source / bad payload
webhook
HMAC verification + audit
Missing, stale, invalid signature
gateway
Dynatrace token -> signed E-Pager request
Missing/invalid gateway token
incident
Create, update, acknowledge, resolve
Duplicate or unauthorized access
escalation
Timed assignment movement
No policy / max level reached
notification
Push provider + delivery tracking
No device / provider failure
security
JWT, refresh token, role access
Invalid token / wrong role
project/user
Admin configuration
Invalid user/project/policy data

## Slide 5
INGESTION PATHS
Alert ingestion has two production paths and one testing simulator path.
E-Pager technical deep dive | Source: project docs and implementation
05
Direct HMAC
Monitoring tool
Tool can generate
X-EPAGER-SIGNATURE
/api/alerts/{source}
HMAC timestamp + signature required
Gateway path
Dynatrace
Can send static header
cannot sign dynamic HMAC
/gateway/webhooks/dynatrace
Validate static bearer token
create HMAC
/api/alerts/dynatrace
Receives signed internal request
Simulator
/api/testing/alerts/{source}/critical
Generates realistic payload
uses real AlertService
Incident + notification
Demo without external tool
Cross-question answer
The simulator is not a production monitoring input. It is a protected admin/manager test API that calls the same internal alert pipeline to prove the behavior.

## Slide 6
UNIFIEDALERT CONTRACT
Vendor JSON changes are absorbed at the adapter layer, not in the incident engine.
E-Pager technical deep dive | Source: project docs and implementation
06
Grafana JSON
alerts[0].fingerprint
labels.projectKey
labels.service
annotations.summary
Dynatrace JSON
problemId
problemTitle
impactedEntity
tags.projectKey
UnifiedAlert
source
externalAlertId
projectKey
groupKey
serviceName
severity
title
description
Core logic
IncidentService
EscalationService
NotificationService
No vendor assumptions
adapter
adapter
stable contract
Why not raw JSON everywhere?
Every service would need vendor parsing, tests would multiply, and adding a new tool would risk breaking core incident behavior.

## Slide 7
INCIDENT LIFECYCLE
The incident state machine is small by design, and every transition has a guard.
E-Pager technical deep dive | Source: project docs and implementation
07
TRIGGERED
Created from alert
assigned to current level
eligible for escalation
ACKNOWLEDGED
Engineer/admin/manager accepts ownership
escalation stops
RESOLVED
Incident completed
no more escalation
acknowledge
resolve
Scenario
Positive behavior
Negative behavior
New alert
Create incident, set TRIGGERED, assign level 1
Unknown source/security fail stops before incident
Duplicate active alert
Update existing incident by source + externalAlertId
Avoids duplicate paging storm
Engineer access
Can see assigned incident
403 if incident assigned to someone else

## Slide 8
ESCALATION MATRIX
Escalation converts policy into timed ownership changes until someone acknowledges.
E-Pager technical deep dive | Source: project docs and implementation
08
Level 1
Shivam Engineer
immediate assignment
Level 2
Ravi Lead
after 5 min if still TRIGGERED
Level 3
Manish Manager
after 10 more min
no ack
no ack
Positive scenario
Shivam acknowledges before nextEscalationAt.
Result: status becomes ACKNOWLEDGED; scheduled job ignores it.
Negative scenario
No one acknowledges before wait time.
Result: scheduled escalation moves to next level and records EscalationEvent.
Boundary scenario
No more levels available.
Result: incident remains TRIGGERED; event history shows max-level behavior. Future roadmap: on-call rotations.

## Slide 9
NOTIFICATION DELIVERY
We track the notification lifecycle separately from the incident lifecycle.
E-Pager technical deep dive | Source: project docs and implementation
09
QUEUED
Log row created before provider call
SENT
Provider accepted push request
RECEIVED
Client app confirms device received it
SEEN
User opened notification / incident
FAILED
No device, provider error,
or push provider failure
failure path
Question
Answer
How know sent?
NotificationLog status SENT + providerMessageId
How know reached?
Client calls /received after push event
How know user opened?
Client calls /seen from notification click/deep link

## Slide 10
ROLE SECURITY
RBAC follows operational responsibility: configure, manage, respond.
E-Pager technical deep dive | Source: project docs and implementation
10
Role
Allowed
Blocked / negative scenario
ADMIN
Manage users, projects, webhook sources, escalation policies; view incidents and notifications
Still needs valid JWT; invalid/expired token rejected
MANAGER
Manage escalation policies and incidents; view notification logs
403 from admin-only users/projects/webhooks
ENGINEER
View, acknowledge, resolve assigned incidents; track own notification path
403 if accessing admin APIs or unassigned incidents
Cross-question answer
Engineers cannot spoof acknowledgement user IDs. For engineer actions, the backend uses the authenticated current user, not a request body user ID.

## Slide 11
JWT HARDENING
Authentication is split into short-lived access tokens and revocable refresh tokens.
E-Pager technical deep dive | Source: project docs and implementation
11
Login
email + password
BCrypt check
Access token
JJWT signed
claims: userId, email, role
Refresh token
Opaque random token
DB stores SHA-256 hash only
Refresh
Old token revoked
new pair issued
Scenario
Positive result
Negative result
Valid access token
Request authenticated with role
Wrong role returns 403
Refresh token used once
Rotates and returns new token pair
Reused/expired/revoked token returns 401
Password changed
Password hash updated
All active refresh tokens revoked

## Slide 12
WEBHOOK SECURITY
Public alert APIs are open at Spring Security level but protected by HMAC and source configuration.
E-Pager technical deep dive | Source: project docs and implementation
12
Check
Positive path
Negative path
Source enabled
WebhookSource found and enabled
401: source not configured/enabled; audit rejected
Timestamp
Instant parse succeeds and within 5 minutes
401: missing, malformed, or stale timestamp
Signature
HMAC_SHA256(secret, timestamp + ':' + rawBody) matches
401: invalid/missing signature
Audit
Accepted audit row is stored
Rejected audit row is stored using noRollbackFor
Why HMAC instead of a fixed token?
A fixed token can be replayed if leaked. HMAC signs the exact body plus timestamp, so tampering or replay outside the time window fails.

## Slide 13
DYNATRACE GATEWAY
The gateway translates a static Dynatrace webhook into E-Pager's dynamic HMAC contract.
E-Pager technical deep dive | Source: project docs and implementation
13
Dynatrace
Sends custom problem notification
Authorization: Bearer token
Gateway endpoint
POST /gateway/webhooks/dynatrace
validate static token
Gateway service
generate timestamp
calculate HMAC over raw JSON
Alert API
POST /api/alerts/dynatrace
normal flow
bearer
raw JSON
HMAC
Scenario
Result
Missing/invalid gateway token
401 before forwarding; no incident created
Valid gateway token + valid payload
Gateway signs payload; alert API validates; incident + notification created
Gateway secret mismatched with webhook source
Forward happens but alert API rejects HMAC; audit shows rejection

## Slide 14
SIMULATION API
The simulator is a safe demo trigger that exercises the real pipeline without external tooling.
E-Pager technical deep dive | Source: project docs and implementation
14
POST /api/testing/alerts/dynatrace/critical
ADMIN or MANAGER
creates realistic Dynatrace JSON
POST /api/testing/alerts/grafana/critical
ADMIN or MANAGER
creates realistic Grafana JSON
AlertService
Uses real source adapter
no duplicated incident logic
Incident + notification
TRIGGERED incident
Shivam assigned
push log created
Cross-question answer
This endpoint mocks the monitoring tool's POST, but still uses the real adapter, incident, escalation, and notification services. It should stay protected and should not be exposed as a public production alert endpoint.

## Slide 15
MANUAL SWAGGER DEMO
A reliable demo follows the same path every time.
E-Pager technical deep dive | Source: project docs and implementation
15
Step
Action
Expected proof
1
POST /api/auth/login as admin
accessToken + refreshToken returned
2
Swagger Authorize with Bearer accessToken
protected endpoints become callable
3
GET /api/users and /api/escalation-policies
seeded users and matrix visible
4
POST /api/testing/alerts/dynatrace/critical
incident returned as TRIGGERED
5
GET /api/notifications
notification log exists for incident
6
POST /received then /seen
delivery timeline proves reached/opened
7
POST /acknowledge then /resolve
incident lifecycle completes

## Slide 16
AUTOMATED TESTING
Current tests already cover role security, auth hardening, simulator behavior, and rejected webhook audit.
E-Pager technical deep dive | Source: project docs and implementation
16
Implemented tests
- Admin/manager/engineer access
- Engineer assigned incident rules
- Protected endpoint blocking
- Gateway missing-token rejection
- User creation password validation
- Refresh-token rotation
- Password-change revocation
- Rejected webhook audit
- Simulator creates incident + notification
Next high-value tests
- Valid Grafana HMAC creates incident
- Valid Dynatrace HMAC creates incident
- Expired timestamp rejected
- Disabled source rejected
- Adapter mapping unit tests
- Escalation scheduler tests
- FCM provider mocked tests
Why PostgreSQL integration tests?
- Flyway schema validated
- JPA mapping is real
- token/audit/notification persistence verified
- behavior closer to production than H2
- catches transaction rollback bugs
Latest verified state: 10 integration tests passed after adding the alert simulation API.

## Slide 17
REAL PUSH READINESS
To notify real phones or browsers, the backend needs real client device tokens.
E-Pager technical deep dive | Source: project docs and implementation
17
Mobile/Web app
Uses Firebase/Web Push SDK
gets registration token
Register device
POST /api/users/{id}/devices
platform + pushToken
E-Pager DB
Stores active UserDevice
FCM provider
Sends real push
when enabled
Need
Backend status
Still required
Firebase provider
Implemented behind EPAGER_FIREBASE_ENABLED
Firebase project and service-account JSON
Device token storage
Implemented via user_devices
Real mobile/web client to register token
Notification open tracking
Implemented /received and /seen
Client SDK must call these APIs

## Slide 18
CLIENT SDK RESPONSIBILITIES
The SDK/app is not the pager backend; it is the user's notification receiver and tracker.
E-Pager technical deep dive | Source: project docs and implementation
18
Responsibility
Where it lives
Positive behavior
Negative scenario
Login/session
App/SDK + E-Pager auth
Stores access/refresh securely
Expired token -> refresh; invalid refresh -> login
Device registration
App/SDK
Gets FCM/Web Push token and registers device
No token -> backend cannot send real push
Receive push
OS/browser + app
Displays notification with deep link
OS permission denied -> user not alerted
Delivery callback
App/SDK
Calls /received when push event arrives
No callback -> backend only knows provider accepted
Open callback
App/SDK
Calls /seen when user taps notification
No callback -> cannot prove user opened
Answer to 'do we put SDK on every mobile?': yes, every client/device that must receive push needs app/SDK registration so E-Pager has a valid push token.

## Slide 19
CROSS-QUESTION MAP
Most review questions reduce to one of these positive/negative scenarios.
E-Pager technical deep dive | Source: project docs and implementation
19
Area
Positive
Negative
What we can say
Source trust
HMAC/gateway token valid
missing/stale/bad signature
Rejected with 401; audit row stored
Payload format
Adapter maps payload
source unsupported
404/400 behavior; core protected from raw vendor drift
Incident
new or duplicate alert handled
unauthorized engineer
idempotent create/update; 403 for unassigned access
Escalation
ack before wait time
no ack
stops on ACK/RESOLVED; otherwise scheduled job escalates
Notification
device exists/provider accepts
no device/provider fails
SENT vs FAILED; delivery events show timeline
Auth
valid JWT/role
expired/reused/wrong role
401/403; refresh tokens rotate and revoke

## Slide 20
PRODUCTION ROADMAP
The backend foundation works; production readiness is about reliability, clients, and operations.
E-Pager technical deep dive | Source: project docs and implementation
20
Now
Backend APIs
PostgreSQL
JWT/refresh
HMAC
testing simulator
Next
More HMAC tests
adapter tests
scheduler tests
FCM mocked tests
Client layer
Mobile/web SDK
device token registration
received/seen callbacks
Production
HTTPS
vault secrets
metrics
retry/outbox
rate limiting
Readiness item
Why it matters
HTTPS + secret management
Protect tokens, HMAC secrets, Firebase credentials
Notification retry/outbox
Avoid losing alerts during provider/network failure
Actuator/metrics/logs
Operate and troubleshoot live pager behavior
Mobile/web client
Real user push notification and delivery tracking
Meeting close: E-Pager is vendor-independent by design; what remains is production hardening and real client rollout.